|  | ......................... pcs. .............................. € .............................. € GEZE overhead door closer TS 5000 L with mechanical hold-open device, in accordance with EN 1154, with guide rail BG, hold-open bracket with precise variable adjustment between 80° and 130°, hold-open position can be overridden; closing force, closing speed, back check and latching action are front adjustable, with visual closing force display, door leaf installation on opposite hinge side ( ) TS 5000 L closer body size EN 2-6, up to leaf width 1400 mm ( ) TS 5000 L ECline closer body size EN 3-5, with very high efficiency > 80% for barrier-free doors in accordance with DIN 18040, up to leaf width 1250 mm Alternative to the guide rail BG with hold-open device: ( ) with T-Stop guide rail BG, with integrated opening restrictor and mechanical hold-open device Colour: ( ) silver-coloured ( ) dark bronze ( ) white ( ) stainless steel optic ( ) acc. to RAL |
| --- | --- |