|  | ......................... pc € .............................. € .............................. Self-locking mechanical locking panic lock set GEZE IQ lock C DL for double-leaf doors with integrated contacts for door surveillance Self-locking mechanical panic lock GEZE IQ lock C DL for the moving leaf with mechanical strike box for the fixed leaf plus all required and tested components for double-leaf full panic doors in accordance with EN 179 and EN 1125! The moving leaf is also unlocked upon panic release of the fixed leaf. Panic unlocking via latch or panic bar Self-locking of both door leaves Changeover function for unlocking from outside Divided and separated cross latch for absolute unencumbered crossbar projection without jamming even when preloaded; steel bolt 20 mm throw IQ lock C DL can be used for DIN left and right doors Prepared for installation of profile lock cylinders and with 9 mm square nut. Closed and corrosion-resistant steel lock case in DIN sizes, front metal and strike box of stainless steel; IQ lock C DL combines well with SHE systems thanks to integrated contacts. All required contacts are integrated in the lock and provide potential-free reporting: Deadbolt contact (with 95 % bolt throw) Latch contact (with latch activation 10°) Cylinder contact Auxiliary lock contact (door open/door leaf enclosed) Supplied in a set comprising: 1 pc mechanical panic lock IQ lock C DL 1 pc mechanical strike box IQ lock DL with front metal 1 pc strike plate for receiving the lock upwards 1 pc switch lock 1 pc tubular pipe for locking upwards 1 pc solid rod for locking downwards 1 pc rod guide 1 pc floor lock hollow ( ) IQ lock C DL 9235 (distance 92 mm, backset 35 mm) ( ) IQ lock C DL 9240 (distance 92 mm, backset 40 mm) ( ) IQ lock C DL 9245 (distance 92 mm, backset 45 mm) ( ) IQ lock C DL 7255 (distance 72 mm, backset 55 mm) ( ) IQ lock C DL 7265 (distance 72 mm, backset 65 mm) ( ) IQ lock C DL 7280 special backset 80 mm ( ) IQ lock C DL 7210 special backset 100 mm For use in escape and rescue routes or in fire protection doors, fittings are required in accordance with EN 179 or EN 1125:. For approved fittings, please refer to the currently valid certificate versions 0757-CPR-229-7013137-5-2 / 0757-CPR-229PANIK-7013137-4 to certify the durability Only GEZE components tested and approved together in accordance with EN 179 and EN 1125 may be installed! Accessories: ( ) 1 pc connecting cable IQ lock part no. 103669 To ensure all functions of the IQ lock C DL a door closer system with closing sequence control and a carry bar are to be fitted. GEZE recommends ( ) 2 pc TS 5000 part no. 027333 ( ) 1 pc ISM gliding rail part no. 115549 and ( ) 2 pc GEZE panic bars (EN 1125) configurable part no. 119005 |
| --- | --- |